## Slide 1: Hydrogen in Australia Martin Hablutzel, 7 May 2019
siemens.com
Unrestricted © Siemens Ltd 2019

## Slide 2: Different storage technologies for different applications – hydrogen for large-scale and long-term energy storage
1 such as Ammonia, Methanol or others;
2 Li-Ion, NaS, Lead Acid, etc.
Duration
Minutes
Seconds
Hours
Weeks
1 kW
Power
100 kW
1 MW
10 MW
100 MW
1,000 MW
Hydrogen & derived chemicals1
Flywheel storage
(< 1MW Flywheel, up to 100 MW Turbines)
Super
capacitor
Flow-
Batteries
Pumped Hydro
Compressed Air
Batteries2
Days
Technology
Mechanical
Electrical
Electrochemical
Chemical
Thermal
  Hydrogen can be stored
  cost-effectively
  on a large scale.

## Slide 3
“Yes my friends, I believe that water will one day be employed as fuel, that hydrogen and oxygen which constitute it, used singly or together, will furnish an inexhaustible source of heat and light, of an intensity of which coal is not capable.... When the deposits of coal are exhausted we shall heat and warm ourselves with water. Water will be the coal of the future.”
—Jules Verne, The Mysterious Island (1874-5)

## Slide 4: Proton exchange membrane (PEM) electrolysis – the efficient way for green hydrogen
  Electrodes are attached on both sides of the proton exchange membrane
  Proton exchange membrane is the electrolyte
  Proton exchange membrane acts as separator to prevent mixing of the gas products
How does PEM electrolysis work
Advantages of PEM electrolysis
1973
J. H. Russell released his works to PEM electrolysis and the high potential
  High power density
  Extended dynamic operation range and direct coupling to renewables (rapid response)
  High efficiency
  High gas purities
  Low maintenance needs

## Slide 5: Hydrogen from renewables enables large scale long term storage and sector coupling.
Photovoltaic
Wind Power
Industry (eg Ammonia, Synthetic Fuels)
Mobility
Electricity System Resilience
PEM electrolysis
Variable electricity generation
Grid integration
Conversion/ storage
Applications
H2 storage and distribution
Grid
Stabilisation
Export
Gas Network

## Slide 6: There are different applications for green hydrogen in Industry, Mobility and Energy
Segment | Application | Description
Industry | Ammonia production | Onsite H2 production from renewable energy replacing Steam methane reforming (SMR) or coal gasification or substitute trailers for industrial processes like ammonia production, petroleum refinement, metal production, glass industry, specialty refineries, food & beverage, chemical industry etc.
 | Petroleum refinement | 
 | Metal production | 
 | Other industries | 
Mobility | Alternative fuel | Using hydrogen as fuel for fuel cell vehicles (FCV) for long distance in parallel to BEV for short to medium distance; Reduction of CO2 footprint for individual, public and commercial transport
 | Green fuels | Using hydrogen to create green fuels (hydrocarbon mixtures) substituting or adding to fossil sources of power (e.g., like 1st/2nd gen biofuels being added to gasoline)
Energy | Hydrogen blending (gas grid) | Substitute up to 10% Methane/NG in the gas-grid by feeding in hydrogen
 | Re-electrification | Provide energy by re-electrification of green H2 (supplied by trailer or produced on-site) in remote/off-grid areas and/or substitution of diesel generators and batteries
Add on | Grid services | Using electrolysis as load to provide primary and secondary control power
 | Energy storage | Absorb peak production by storing renewable energy as H2 instead of curtailment
 | Energy export | Export renewable energy with liquid H2 ; Ammonia or other hydrogen carrier (e.g. LOHC, LH2)
+

## Slide 7: Hydrogen business case depends on the application.
Source: Australian National Hydrogen Roadmap, CSIRO https://www.csiro.au/en/Do-business/Futures/Reports/Hydrogen-Roadmap August 2018.

## Slide 8: Silyzer 200 High-pressure efficiency in the megawatt range
20 kg
Hydrogen production per hour
5 MW
World’s largest operating PEM electrolyzer system in Hamburg, Germany
1.25 MW
Rated stack capacity
60 kWh
Specific energy consumption for 1 kg hydrogen

## Slide 9: Silyzer 300 – the next paradigm in PEM electrolysis
17.5 MW
340 kg
75 %
24 modules
System efficiency (higher heating value)
per full Module Array (24 modules)
Silyzer 300 – Module Array (24 modules)
hydrogen per hour
per full Module Array
(24 modules)
to build a
full Module Array

## Slide 10: Technology scales up by factor 10 every 4-5 years. Lower costs bring new applications into play.
2018 – 2023+
2011 – 2015
2015 – 2018
>2030
Silyzer 100 100 – 300 kW
Lab-scale
Silyzer 300 >10 MW class
Released 2018
>1,000 MW
First investigations in cooperation with chemical industry
Next generation Silyzer >100 MW
Under development
Silyzer 200 1 MW class
Commercial product
Reduction of H2 production cost ($/kg H2)
Notes: Development focus:
Large scale, industrial hydrogen plant concepts
Lowest specific cost
Fleet data digitalization

## Slide 11: Energiepark Mainz World’s largest PEM electrolysis facility in 2015
Facts & figures
Customer: Energiepark Mainz (JV of Linde and Mainzer Stadtwerke)
Country: Germany
Installed: 2015
Product: Silyzer 200
3.75 MW
rated power / 6.0 MW peak power (limited in time) based on three Silyzer 200
Green hydrogen is fed into the local natural gas grid.
Use cases
Challenge
Installation of three SILYZER 200 with a maximum power consumption of 6 MW
Highly dynamic power consumption
State-of-the-art process control technology based on SIMATIC PCS 7
Hydrogen processing, condensing, and storage (provided by Linde)
Installation of world’s first PEM electrolysis plant in the multiple megawatt range
Provision of balancing energy
High degree of automation
Solutions
Hydrogen for regional filling stations.
Delivery to surrounding industrial companies.

## Slide 12: South Australia – Australian Gas Infrastructure Group Largest PEM electrolyser in Australia
Facts & figures
Customer: AGIG
Country: Australia
Installed: under delivery
Product: Silyzer 200
Green hydrogen is fed into the local gas network.
Use cases
Challenge
Operation of a SILYZER 200
Highly dynamic power consumption
State-of-the-art process control technology based on SIMATIC PCS 7
Installation and integration into the local gas network
Remote control of electrolyser to integrate with local microgrid and solar power generation
Potential for future addition of refueling facility and/or tube trailer
Solutions
Future plans to add refueling capability.
1.25 MW
rated power based on Silyzer 200

## Slide 13: Hydrogen industry development Sustainable pipeline of scale projects domestically will build industry capability and accelerate commercialisation for export.
Investment projects
“double-digit”
Example applications:
Energy grid stabilisation
RAPS
Mobility (eg cars/buses)
Gas grid injection
Industrial
Project Scale
2025+
2018
2020
2022
Tonsley, ATCO, Jemena
Very large scale commercial export projects
Early export projects
>100MW
Subsidy per MW*
>5$m per MW
~$2.5m per MW
<$1m per MW
~$0m per MW**
*Subsidy expressed as total project costs / MW electrolyser installed
** Low-cost finance and carbon pricing impact may be considered as ‘subsidies’

## Slide 14: Contact page
Martin Hablutzel Head of Strategy
885 Mountain Highway Bayswater VIC 3153
Mobile: +61 (0)408 383 891
E-Mail: martin.hablutzel@siemens.com
siemens.com